GreenLine™ EMS – Engine Monitoring System

The GreenLine™ EMS is a complete Engine Monitoring System designed to provide the pilot with easy-to-read numerical engine data, warning messages in the event of out-of-tolerance engine conditions, and a quick-scan, tricolor system of solid bar indicators for critical engine parameters.  The result is a simple, attention-getting visual display to direct your attention to out-of-limit engine conditions and back it up with clear, digitally displayed data.

The GreenLine's primary screen displays numerical values for:

- Engine RPM

- Manifold Pressure

- Oil Temperature

- Oil Pressure

- Fuel Pressure

- Hottest Cylinder-Head Temperature

- Hottest Exhaust Gas Temperature

If a critical engine parameter is out of tolerance, a flashing warning message is immediately displayed on the GreenLine's large-character LCD screen.

By pressing the "Change Screen" button on the GreenLine's front panel, the pilot can view the following clearly identified numerical engine data:

- Cylinder Head Temperatures for Cylinders 1 and 2

- Exhaust Gas Temperatures for Cylinders 1, 2, 3 and 4

- Outside Air Temperature

- Voltage

- Fuel Flow

- Duration of Flight Time

- Total Cumulative Engine Time

In addition, bright, clearly labeled green, amber and red bar indicators provide normal, cautionary and warning indications of these critical engine parameters:

- Engine RPM

- Oil Temperature

- Oil Pressure

- Fuel Pressure

- Hottest Cylinder Head Temperature

- Hottest Exhaust Gas Temperature

Additional Specifications:

Width: 6.25 inches (exact radio-rack width)

Height: 3.1 inches

Depth: Approximately 5.5 inches

Total weight: Approximately 2 lbs.

Available in Imperial or Metric units